Introduced by the Council President at the request of the Mayor and amended on the floor of the Council:

ORDINANCE 2007-836-E

AN ORDINANCE RELATING TO STORMWATER MANAGEMENT AND FEES; REPEALING CHAPTER 754 (STORMWATER CODE), ORDINANCE CODE; RE-CREATING A NEW CHAPTER 754 (STORMWATER MANAGEMENT UTILITY CODE) AS A NEW STORMWATER MANAGEMENT UTILITY CHAPTER PURSUANT TO FLA. STAT. SECTION 403.0893; CREATING A NEW PART 1, CONSISTING OF DECLARATIONS, A SCOPE AND INTENT, DEFINITIONS, ESTABLISHMENT OF THE STORMWATER MANAGEMENT UTILITY, A DIRECTOR, DUTIES AND POWERS, AUTHORITY OF STORMWATER MANAGEMENT SERVICE CHARGES FOR THE GENERAL SERVICES DISTRICT OF THE CONSOLIDATED CITY OF JACKSONVILLE, AS SET FORTH IN THE CHARTER OF THE CITY OF JACKSONVILLE, EXCLUDING URBAN SERVICES DISTRICTS 2, 3, 4 AND 5 BEING THE CITIES OF JACKSONVILLE BEACH, ATLANTIC BEACH, NEPTUNE BEACH, AND THE TOWN OF BALDWIN; PROVIDING THE BASIS FOR THE RATE AND THE COLLECTION THEREOF, INCLUDING NON AD VALOREM ASSESSMENTS; ESTABLISHING A STORMWATER MANAGEMENT UTILITY TRUST FUND, APPEALS, DELINQUENT CHARGES, AND ALTERNATIVE METHODS OF COLLECTION; PROVIDING FOR COUNCIL APPROVAL OF RULES, CREDITS AND MITIGATION PROGRAMS; CREATING A NEW PART 2, CONSISTING OF STORMWATER DISCHARGES FROM INDUSTRIAL ACTIVITIES AND CONSTRUCTION SITES, ILLICIT DISCHARGES, REPORTING, CONTROL OF POLUTANT CONTRIBUTION FROM STORMWATER SEWER SYSTEMS CONNECTED TO THE MS4, GENERAL PROHIBITION, EMERGENCY CONDITIONS, LIABILITY FOR POLLUTION ABATEMENT, INDUSTRIAL AND HIGH RISK RUNOFF, INJUNCTIVE RELIEF PROHIBITING DISCHARGE, ENFORCEMENT, PENALTIES AND CIVIL PENALTIES FOR VIOLATIONS OF PART 2, AND AUTHORIZATION TO PROMULGATE RULES; PROVIDING THAT THE HISTORY OF THIS CHAPTER SHALL BE PRESERVED; PROVIDING FOR SEVERANCE; PROVIDING FOR OPTIONS FOR COLLECTION; AND PROVIDING AN EFFECTIVE DATE.

BE IT ORDAINED by the Council of the City of Jacksonville:

Section 1.		Chapter 754 (Stormwater Code) repealed. Chapter 754 (Stormwater Code) is hereby repealed.  A copy of the former chapter 754 is on file with the Legislative Services Division.

Section 2.		New Chapter 754 (Stormwater Management Utility Code) created. A new Chapter 754 (Stormwater Management Utility Code) consisting of Part 1 and Part 2, is hereby created to read as follows:

CHAPTER 754.  STORMWATER MANAGEMENT UTILITY CODE.

Part 1.  Establishment of Utility, Rates, and Enforcement.

Sec. 754.101.  Declaration, intent and scope.

(a)  The City finds and declares the following as the intent and scope of the Stormwater Management Utility Code:

(1) 	To provide for effective management and financing of a stormwater system within the City by establishing a Stormwater Management Utility pursuant to Fla. Stat. 403.0893; and

(2)	To provide that the Stormwater Management Utility Code shall be effective in the General Services District of the Consolidated City of Jacksonville, as set forth in the Charter of the City of Jacksonville excluding Urban Services Districts 2, 3, 4 and 5 being the Cities of Jacksonville Beach, Atlantic Beach, Neptune Beach, and the Town of Baldwin.

(3)  To provide a mechanism for mitigating the damaging effects of uncontrolled and unplanned stormwater runoff; and

(4)	To improve the public health, safety and welfare by providing for the safe and efficient capture and conveyance of stormwater runoff and the correction of stormwater problems; and

(5)  To ensure compliance with the City’s National Pollutant Discharge Elimination System (NPDES) Stormwater permit and to authorize the establishment and implementation of a plan for storm management  including planning, design, coordination, construction, management, regulation, operation, maintenance, inspection, surveying and enforcement; and

(6)  To establish a program of user charges for stormwater management service to be charged to all developed property within the city that contributes stormwater runoff to the city's stormwater management systems to accomplish the functions of such utility; and

(7) 	To encourage and facilitate urban water resources best management techniques, including but not limited to the retention/detention of stormwater runoff, minimization of the need to construct storm sewers, and the enhancement of the environment.

(b) In order to accomplish these purposes, a stormwater service charge shall be made on each developed parcel in the City.

(c) The City's stormwater service charges shall be fair and reasonable, and bear a substantial relationship to the cost of providing service and facilities, in that similar properties shall pay similar stormwater service charges. Rate studies shall be conducted periodically to ensure the equity of the service charges.

Sec. 754.102. Definitions.

As used in this chapter, unless the context otherwise requires:

(a)	Adjusted impervious area shall mean the stormwater basin area(s) multiplied by the stormwater management facility impervious area factor plus the impervious area(s) plus one-half of the partial impervious area(s), as is set forth on Schedule 1.

(b)	Best management practices (BMPs) means those schedules of activities, prohibitions of practices, maintenance procedures, and other management practices to prevent or reduce pollutants from entering the MS4 or being discharged from the MS4 so as to protect or restore the quality of surface waters in Duval County. BMPs include, but are not limited to, treatment methods and practices to control site runoff, spillage, leaks, sludge, waste disposal or runoff from raw material.

(c)	CAO shall mean the Chief Administrative Officer of the City, or the designee thereof.

(d) City shall mean the consolidated City of Jacksonville, Florida, and its staff and elected officials, but shall not include the City of Jacksonville Beach, the City of Atlantic Beach, the City of Neptune Beach, and the Town of Baldwin.

(e)	Department shall mean the Public Works Department of the City.

(f)	Developed property shall mean any parcel of land that has been modified by the action of persons to reduce the land's natural ability to absorb and hold rainfall. These modifications include, but are not limited to, clearing, grading, cementing, filling, or compacting the natural ground, or erecting or constructing buildings, parking lots, driveways, patios, decks, walkways, and athletic courts.

(g)	Director means the Director of the Stormwater Management Utility or his designee.

(h)	Discharge includes, but is not limited to, any spilling, leaking, seeping, pouring, emitting, emptying or dumping of any material, including liquids.

(i)	Drainage area shall mean the watershed (acreage) contributing surface water runoff to the city's storm drainage system.

(j)	Dwelling unit shall mean those living areas served by individual electric and/or water meters.

(k)	Equivalent residential unit (ERU) shall mean the basic unit for the computation of stormwater service charges and is defined as approximately 2443 square feet of impervious area, which represents the estimated average impervious area for all developed, detached single-family properties in the city.

(l)	Illicit connection means any man-made conveyance connecting a non-stormwater discharge directly to a municipal storm sewer system.

(m)	Illicit discharge  means any discharge to a municipal separate storm sewer system that is not composed entirely of storm water except discharges pursuant to a National Pollutant Discharge Elimination System permit (other than the city's NPDES stormwater permit). The term also does not include water line flushing, landscape irrigation, diverted stream flows, rising underground waters, uncontaminated ground water infiltration (as defined at 40 CFR 35.2005(20)) to separate storm sewers, well point water discharges from potable water sources, foundation drains, air conditioning condensate, irrigation water, springs, water from crawl space pumps, footing drains, lawn watering, individual residential car washing, dechlorinated swimming pool discharges, flows from riparian habitats and wetlands, street wash waters, and discharges or flows from emergency fire fighting activities.

(n)	Impervious area shall mean any part of any parcel of land that has an impermeable cover caused to be erected or constructed by the action of persons, and such covers include, but are not limited to, buildings, parking lots, driveways, patios, decks, walkways, and athletic courts.

(o)	Industrial activities  mean activities which are conducted on properties designated for industrial land use according to local comprehensive plans and at facilities identified by the U.S. Environmental Protection Agency as requiring a National Pollutant Discharge Elimination System stormwater permit under the definition of "Stormwater Discharge Associated with Industrial Activity" in 40 CFR 122.26.

(p)	Industrial and high risk runoff  means discharges from landfills, hazardous waste treatment, storage, disposal and recovery facilities, facilities that have reported under the requirements of EPCRA Title 3, Section 313, and any other industrial or commercial discharge which the Director determines is contributing a substantial pollutant loading to the MS4.

(q)	Inspection includes, but is not limited to, a review of all components of a stormwater management system, records on operation and maintenance of facilities and the results of any monitoring performed in compliance with state, federal or local regulations or permit conditions.

(r)	Multifamily residential properties shall mean and include all duplex, condo, trailer, apartment and other properties containing more than one dwelling unit. Common areas associated with such properties shall be included in the charge to the multifamily units on such properties.

(s)	Municipal storm sewer system or MS4 means that conveyance or system of conveyances (including roads with drainage systems, streets, catch basins, curbs, gutters, ditches, man-made channels, pipes, head walls, manholes and storm drains) owned by the City of Jacksonville, designed or used for collecting or conveying storm water, which is not a combined sewer, and which is not part of a publicly owned treatment works as defined in 40 CFR 122.2.

(t)	Nonresidential/commercial properties  shall mean and include all property zoned or used for commercial, industrial, retail, governmental, or other nonresidential purposes and shall include all developed real property in the city not classified as single-family or multifamily as defined in this section.

(u)	Partial impervious area shall mean any part of any parcel of land that has been modified by the action of persons to reduce the land's natural ability to absorb and hold rainfall. This includes areas which have been cleared, graded, graveled, filled, or compacted, and typically involve unpaved parking, unpaved vehicle and equipment storage, and material storage. Excluded are all lawns, landscape areas, and gardens or farming areas.

(v)	Person shall mean any person, firm, individual, partnership corporation, organization of association of any kind.

(w)	Receiving water shall mean those creeks, streams, rivers, lakes, sinkholes, and other bodies of water into which surface waters are directed, either naturally or in manmade ditches, pipes, or open systems.

(x)	Retention credit factor shall mean the numeric value generated by dividing the stormwater retention volume by the standard retention volume, but the value cannot exceed 1.0.

(y)	Single-family property shall mean and include all single-family detached housing units.

(z)	Standard retention volume shall mean the quantity of stormwater runoff generated by multiplying 7.9 inches by the adjusted impervious area.

(aa)	Storm sewer refers to a municipal storm sewer.

(bb)	Stormwater means stormwater runoff, surface runoff and drainage.

(cc)	Stormwater basin area shall mean the horizontal area occupied by stormwater detention, retention, and/or detention/retention basins at the design maximum water surface elevation.

(dd)	Stormwater detention basin shall mean a facility, either natural or manmade, that collects and contains stormwater runoff and allows the release of the stormwater through a structure that is designed to control the rate of the release of the stormwater, as acknowledged by the city manager or designee.

(ee)	Stormwater detention/retention basin shall mean a facility, either natural or manmade, that performs a combination of both a stormwater detention basin and a retention basin, as acknowledged by the city manager or designee.

(ff)	Stormwater management facility impervious area factor shall mean the amount that the stormwater retention basin area(s) is adjusted; the factor is derived by dividing 4.2 inches (which is the amount of rainfall generated by the 25-year, 24-hour rain storm event between the 11th and 13th hours) by 7.9 inches (which is the amount of rainfall generated by the 25-year, 24-hour rain storm event) which quotient is 0.53.

(gg)	Stormwater management system shall mean and include all natural and manmade elements used to convey stormwater from the first point of impact with the surface of the earth to a suitable receiving water body or location internal or external to the boundaries of the city. The stormwater management system includes all pipes, channels, streams, ditches, wetlands, sinkholes, detention/retention basins, ponds, and other stormwater conveyance and treatment facilities.

(hh)	Stormwater retention basin shall mean a facility, either natural or manmade, that collects and contains stormwater runoff and only allows the release of the stormwater runoff by one or more of the following: evaporation, percolation into the natural ground and/or percolation into a manmade filtration system that may convey the stormwater runoff to a stormwater management system, as acknowledged by the city manager or designee.

(ii)	Stormwater retention volume shall mean the maximum capacity of a stormwater retention basin(s).

Sec.754.103. Stormwater Management Utility--Established.

There is hereby created and established in the city a stormwater management utility in accordance with Florida Statutes section 403.0893. This utility shall constitute the storm water management system; shall operate from within the Department of Public Works; and shall be responsible for the city's stormwater management plan, subject to appropriations from the City Council.

Sec.754.104. Stormwater Management Utility Director.

The Director of Public Works shall serve as the director of the City’s stormwater management utility.

Sec.754.105 Stormwater Management Utility Director -- Duties and powers.

The stormwater management utility director shall have all powers necessary for the exercise of responsibility of the drainage of stormwater from all properties with the City covered by this Chapter, including, but not limited to, the following:

(a)   Preparation of plans for improvements and betterments to the stormwater management system.

(b)   Construction of improvements and betterments to the stormwater management system.

(c)   Promulgation of regulations for the use of the stormwater management utility and system, including provisions for enforcement of such regulations.

(d)   Review and approval of all new development permits within the city for compliance with stormwater management regulations included in present city ordinances or ordinances later adopted.

(e)   Performance of routine maintenance and minor improvement to the stormwater management system.

(f)   Establishment of charges, with approval of City Council, for the city's stormwater management utility and system.

(g)   Evaluation of water quality concerns for discharges to the stormwater management system.

(h)   Performance of all normal utility functions to include construction, operation, and maintenance of the city's stormwater management system, including, but not limited to, the hiring of staff, the selection of special consultants, the entering into contracts for services and construction of facilities, and the handling of purchase, lease, sale or other rights to property for the stormwater management system; all consistent with the personnel and procurement requirements of the City.

(i)   Recommendation of the issuance of revenue bonds for the purpose of performing those duties as described herein.

Sec.754.106. Authority for service charges, and for the levy, collection and enforcement thereof.

(a)   Authorization.  The City Council is empowered by this chapter to establish, upon recommendation of the Storm Water Management Director, charges for the use and discharge to the city's stormwater management system. Such charges shall be based on the cost of providing stormwater management services to all properties within the General Services District of the Consolidated City of Jacksonville, as set forth in the Charter of the City of Jacksonville, excluding Urban Services Districts 2, 3, 4 and 5 being the Cities of Jacksonville Beach, Atlantic Beach, Neptune Beach, and the Town of Baldwin.  These charges may be different for properties receiving different classes of service.  As of 2007, the cost of providing stormwater services is approximately thirty four million dollars ($34,000,000).

(b)   Rates for stormwater management service.  There will be a charge for all owners or occupants of real property in the city covered by this ordinance, who have improvements or uses thereon which contribute stormwater runoff to the city's stormwater management system, a monthly stormwater service charge.  The basic stormwater service charge shall be five dollars per month ($5.00), or sixty dollars per year, as follows:

| Single Family detached Residential between 1800 to 3400 square feet | 1 ERU | $5.00 per month |
| --- | --- | --- |
| Single Family detached Residential Less than 1800 square feet | .5 ERU | $2.50 per month |
| Single Family detached Residential Greater than 3400 square feet | 1.5 ERU | $7.50 per month |

All others properties shall be calculated based on the following calculation:

Square footage of impervious land divided by 2443 equals the billing unit.  The number of billing units x $5.00 per month will be the property stormwater service charge.

(c)   Application to certain developed properties.  Service charges shall apply to all developed properties covered by this ordinance within the city using the city's stormwater management system, including those properties classified as nonprofit or tax-exempt for ad valorem tax purposes. Service charges shall apply to all government properties, including properties of the city, including the city-owned buildings, parks, and other properties.

(d)	Undeveloped property.  Stormwater service charges shall not be charged to undeveloped property that has not been altered from the natural state as defined herein, "impervious area" and "partial impervious area." Properties dedicated exclusively to farmland, gardens, and landscaped areas shall also be exempt except for any roads, parking, or structures associated therewith.

(e)   Levy, collection and payment—alternative methods.

(1)	Effective July 1, 2008 through September 30, 2008, the stormwater service charges authorized or imposed by this ordinance shall be charged on an annual basis, and billed on an annual basis and may be charged and collected in advance. The method of billing shall be through any legally authorized method approved by the Stormwater Management Utility Director.

(2) 	For the collection of stormwater service charges incurred as of October 1, 2008 and thereafter, the levy, collection and enforcement of stormwater service charges shall be through the same methodology and procedures as provided for in subsection (e)(1) but shall be collected through the Tax Collector’s Office through methods and at a cost mutually agreed upon between the City and the Tax Collector.

Sec.754.107 Stormwater Management Utility Trust Fund.

(a)   A stormwater management utility trust fund is hereby established into which all revenues from user stormwater service charges, grants, or other funding sources shall be deposited and from which all expenditures related to the city's stormwater management utility shall be paid. All disbursements therein are hereby appropriated and shall not lapse but shall carryover into each succeeding fiscal year.  Accounting and reporting procedures shall be consistent with state law and reported to the City Council by the Stormwater Management Utility Director or designee on an annual basis.

(b)   Expenditures from the fund for activities that are not related to the city's stormwater management utility shall not be permitted, except for prorated charges for general city and central service costs.

Sec.754.108 Appeals.

Any customers or property owners who feel that the stormwater service charge for their property, or any credit therefore, has been assigned or computed incorrectly may petition in writing to the Chief Administrative Officer or designee for a review of such charges.  All such appeals shall be as set forth in the Stormwater Manual.

Sec.754.109.	Council Approval. No stormwater rules or credits and or mitigation programs shall be implemented unless approved by the City Council.

Part 2. Violations and Prohibited Activities

Sec. 754.201. Stormwater discharges from industrial activities and construction sites.

(a)	Using best management practices, stormwater from construction sites shall be controlled to retain sediment on-site and prevent violations of state water quality standards. All erosion and sediment controls required under the pollution prevention plan of a National Pollutant Discharge Elimination System permit for construction, required by a stormwater permit issued by the Florida Department of Environmental Protection or the St. Johns River Water Management District, or required by a city permit or approved construction plan shall be properly implemented, maintained and operated. The minimum requirements for controlling stormwater run-off from construction sites are specified in the City Land Development Procedures Manual and its standard specifications and details.

(b)	Stormwater from areas of construction activity shall be treated or managed on-site, using best management practices, before being discharged to an MS4 or to surface waters. All stormwater discharges from the site shall be of a quality which will not adversely impact the water quality or the beneficial uses of the receiving water.

(c)	Owners and operators of industrial facilities and/or construction sites that will discharge stormwater to an MS4 shall notify the Office of the City Engineer, in writing, before the discharge begins. The noticed discharge shall not begin earlier than 5:00 p.m. of the next municipal working day after the City Engineer's Office receives the notice.

(d)	Any person who has been issued an NPDES permit authorizing discharges to the MS4 shall submit a complete copy of the permit to the city NPDES coordinator, within 60 days after the effective date of this chapter, or 60 days after the issuance, of the permit.

Sec. 754.202. Illicit discharges; reporting.

Illicit discharges to the MS4 are prohibited. Within seventy-two hours after discovering an illicit discharge, persons responsible for the discharge shall report the discovery to the City Engineer's Office. Initially, the report may be by telephone, but the person responsible shall submit a written report within seventy-two hours of discovery. The report shall include a description of the discharge volume, content and frequency; the location of the point of discharge to the MS4; the measures taken or to betaken to terminate the discharge; and, the name, address and telephone number of the person who may be contacted for additional information.

Sec. 754.203. Control of pollutant contributions from stormwater sewer systems connected to the MS4.

The discharge of stormwater between interconnected state, or other municipal storm sewer systems shall not impair the quality of the discharge from the MS4. Owners of sections of a storm sewer connected to the MS4 are responsible for the quality of discharge from their portion of the system and shall coordinate with owners of downstream segments before beginning to modify their system segments.

Sec. 754.204. General prohibition.

In addition to illicit discharges, discharge of spills and the dumping and disposal of materials other than stormwater, including, but not limited to, industrial and commercial wastes, commercial car wash wastes, sewage, garbage, yard waste, trash, petroleum products (including used motor vehicle fluids), leaf litter, grass clippings, and animal wastes), into the MS4 whether directly or indirectly, are prohibited, unless authorized under a NPDES permit.

Sec. 754.205. Correction and discontinuance of prohibited discharges.

(a)   The Stormwater Management Utility Director may order the correction of any unsafe, nonconforming or unauthorized condition which violates any provision of this chapter, or rule adopted hereunder. The Director may also order discontinuance of any activity causing such condition.

(b)   Whenever the Stormwater Management Utility Director orders the correction or discontinuance of any condition or activity on any premises pursuant to this section, the Director shall notify the owner or other person responsible for the condition or activity in writing which notice shall state the nature of the violation, direct the person to correct or discontinue the condition or activity, and provide a reasonable time for the satisfactory correction thereof. Within the time specified in the notice, the responsible person shall permanently cease or correct all violations. Failure to comply with such an order shall constitute a violation of this chapter.

Sec. 754.206. Emergency conditions.

Notwithstanding any other provisions of this chapter, whenever the Stormwater Management Utility Director determines that conditions or activities exist requiring immediate action to protect public health, safety or welfare, or to provide for compliance with this ordinance, rules promulgated hereunder, the terms of the City's NPDES permit conditions or the stormwater control conditions of any City-issued permit or City approved construction plan, City forces are authorized to enter at a reasonable time in or upon any property for the purpose of testing, inspecting, investigating, measuring, sampling and correcting such emergency conditions. Failure to admit personnel responding to emergency conditions, as determined and authorized by the Director, shall constitute a separate violation of this chapter.

Sec. 754.207. Liability for pollution abatement.

Any person responsible for illicit discharges, or noncompliance with best management practices at industrial and/or construction sites, and who fails to correct any prohibited condition or discontinue any prohibited activity at the order of the Director shall be liable to the City for the expenses incurred in abating pollution, including expenses incurred in testing, measuring, sampling, collecting, removing, treating, and disposing of the polluting materials and preventing further noncompliance and/or illicit discharges.

Sec. 754.208. Industrial and high risk runoff.

Within the schedule established under the city's joint National Pollutant Elimination Discharge System stormwater permit, the Director shall identify and develop a program to control pollutants in stormwater discharges to the MS4 from industrial and high risk runoff sources. In developing a control strategy, the Director may rely on data submitted by industrial facilities to state and federal environmental regulatory agencies in satisfaction of their state and/or federal discharge permits. If such data is inadequate for developing a pollutant control program for industrial and high risk runoff sources, the Stormwater Management Utility Director may require such sources to conduct self-monitoring.

Sec. 754.209. Injunctive relief prohibiting discharge.

Immediately upon discovering an ongoing or potential illicit discharge or noncompliance with best management practices to control erosion and/or sediment deposition at construction sites and/or industrial activities, the Stormwater Management Utility Director, in the name of the city, is authorized to apply to the Circuit Court for an injunction. The court shall have jurisdiction, upon a hearing and for sufficient cause shown, to grant a permanent injunction restraining a person from violating this chapter and rules adopted hereunder, or from failing or refusing to comply with an order of the Stormwater Management Utility Director. The city shall be entitled to reasonable attorney's fees and costs, including appellate fees and costs, in an action where the city is successful in obtaining affirmative relief.

Sec. 754.210. Enforcement.

(a)   In addition to the remedies set forth in Section 754.209, this chapter may be enforced by the Stormwater Management Utility Director pursuant to authority granted herein as follows:

(1)   By citation for civil penalties pursuant to the authority granted by F.S. Ch. 162, Part II, and Ch. 609, Ordinance Code; and

(2)   By action for injunctive relief, for civil penalties in the amount of $500.00 for each day of violation, or both, through a court of competent jurisdiction.

(b)	This chapter may also be enforced by law enforcement officers of the Jacksonville Sheriff's Office as provided in Section 754.211(a).

(c)	The Stormwater Management Utility Director is authorized to enter into consent orders and compliance plans to administratively resolve violations or alleged violations.

Sec. 754.211. Penalties; civil penalties.

(a)	Any person who violates any provisions of Part 2 of this chapter shall be guilty of a class D offense; however, the violator may be punished by a fine, either alone or in addition to the imprisonment that may be imposed for class D offenses, not to exceed two thousand dollars a day.

(b)	Municipal code enforcement pursuant to chapter 609, Ordinance Code, is supplemental to enforcement taken by the Director or law enforcement officers.

(c)	Violations of this part shall be punishable by a civil penalty of not more than two thousand dollars for the first offense and of not more than two thousand dollars for each offense thereafter.

(d)	Each day during any portion of which such violation occurs shall constitute a separate offense.

(e)	The remedies and penalties provided in this chapter are not exclusive, and the city may seek whatever other remedies are authorized by statute, at law or in equity, against any person who violates the provisions of this chapter.

Sec. 754.212. Rules.

The Stormwater Management Utility Director is authorized to promulgate rules pursuant to part 2, chapter 100, Ordinance Code, as appropriate to further implement this chapter.

Section 3. 	Commencement of Charges. The stormwater management utility charges authorized in this ordinance shall commence with services provided on and after July 1, 2008.

Section 4. 	Alternative Means of Collection. If for any administrative or legal reason the stormwater management service fees authorized or imposed by this ordinance are not able to be collected in advance under section 754.106(e)(2) for any year of service, then in that event the fees incurred for services provided may be collected as authorized by section 754.106(e)(1).

Section 5. 	Severability. If any section, subsection or provision of this ordinance is held invalid, the remainder shall not be affected by such invalidity.

Section 6.		Effective Date.		This ordinance shall become effective upon signature by the Mayor or upon becoming effective without the Mayor’s signature.

Form Approved:

____/s/ Margaret M. Sidman__________

Office of General Counsel

Legislation Prepared By:	Cindy A. Laquidara

G:\SHARED\LEGIS.CC\2007\ord\Stormwater Ch  754 Enrolled.docb