Introduced by the Council President at the request of the Mayor:

ORDINANCE 2012-214

AN ORDINANCE CONCERNING WIND ZONES AND THE FLORIDA BUILDING CODE; AMENDING SECTION 320.103 (WIND ZONES), PART 1 (ADMINISTRATION; TITLE, PURPOSE AND SCOPE), CHAPTER 320 (GENERAL PROVISIONS), AND SECTION 321.101 (ADOPTION OF APPENDICES), CHAPTER 320 (ADOPTION OF BUILDING CODE), ORDINANCE CODE TO UPDATE WIND ZONES AND REFERENCES TO THE FLORIDA BUILDING CODE APPENDICES CONSISTENT WITH RECENT CHANGES TO THE FLORIDA BUILDING CODE; PROVIDING AN EFFECTIVE DATE.

BE IT ORDAINED by the Council of the City of Jacksonville:

Section 1.		Section 320.103 (Wind zones) amended. Section 320.103 (Wind zones), Part 1 (Administration; Title, Purpose and Scope), Chapter 320 (General Provisions), Ordinance Code, is hereby amended in part as follows:

CHAPTER 320. 	GENERAL PROVISIONS.

PART 1. ADMINISTRATION; TITLE, PURPOSE AND SCOPE

* * *

Sec. 320.103.	  Wind zones.

For purposes of structural design, the location of the 120 mph wind line for the City of Jacksonville shall be as follows: Starting at the intersection of Phillips Highway and the Duval County line at the south, proceed north along Phillips Highway to the intersection of State Road 9A. Proceed north along State Road 9A to the intersection of J. Turner Butler Boulevard. Proceed east along J. Turner Butler Boulevard to a point 4,115 feet east of the midpoint of the intersection of State Road 9A and J. Turner Butler Boulevard. Proceed northerly to the southern terminus of Regent Boulevard. Proceed north along Regent Boulevard to the intersection of Central Parkway. Proceed north along Central Parkway to the intersection of Beach Boulevard/U.S. 90. Proceed west along Beach Boulevard/U.S. 90 to the intersection of State Road 9A. Proceed north along 9A to Yellow Bluff Road. Proceed north along Yellow Bluff Road to Highway 17. Proceed north along Highway 17 to the Duval County line. All structures located east of this line shall be considered in the Wind-Borne Debris Region as defined by the Florida Building Code. All structures west of this line shall be designed for 119 mph three-second gust.

The Florida Building Code specifies three different Risk Categories of structures for Ultimate Design Wind Speed and provides a different wind speed map for each category.  The Florida Building Code also requires each municipality to set the location of the wind speed demarcation lines by ordinance using recognizable physical landmarks.  At the south end of Duval County, the demarcation line shall start in the middle of the St. Johns River at the south end of Duval County, run north up the center of the St. Johns River to the intersection of the St. Johns River and Interstate 95 on the Fuller Warren Bridge, then proceed north along Interstate 95 to the northern Duval County line.

For Risk Category I structures as set forth in the Florida Building Code, the wind speed west of the demarcation line shall be 115 miles per hour and east of the demarcation line 120 miles per hour.

For Risk Category II structures as set forth in the Florida Building Code, the wind speed west of the demarcation line shall be 125 miles per hour and east of the demarcation line 130 miles per hour.

For Risk Category III and Risk Category IV structures as set forth in the Florida Building Code, the wind speed west of the demarcation line shall be 135 miles per hour and east of the demarcation line 140 miles per hour.

An applicant for a building permit may choose to interpolate from the actual wind speed maps instead of using those parameters noted above.  In such instance a location map with the wind speed interpolation calculations shall be provided by a licensed engineer or architect.

* * *

Section 2.		Section 321.101 (Adoption of Appendices) amended.  Section 321.101 (Adoption of Appendices), Chapter 321 (Adoption of Building Code), Ordinance Code, are hereby amended in part as follows:

CHAPTER 321. 	ADOPTION OF BUILDING CODE.

Sec. 321.101.	  Adoption of Appendices

The following appendices are hereby adopted as part of this building code:

* * *

Florida Building Code--Residential Appendices A, B, C, E, F, G, and O

Florida Building Code--Existing Building Appendices B, C, and D

* * *

Florida Building Code-Fuel Gas Appendices A, and B and C

* * *

Section 3.		Effective Date.  This ordinance shall become effective upon signature by the Mayor or upon becoming effective without the Mayor's signature.

Form Approved:

/s/ Dylan T. Reingold____________

Office of General Counsel

Legislation Prepared By:	Dylan T. Reingold

G:\SHARED\LEGIS.CC\2012\Ord\LAND USE GENERAL\Building Code and Wind loads.doc