### M E M O R A N D U M

DATE:	08/21/2014

TO:		Bruce Lewis

City Planner Supervisor

FROM:	Soliman Peter Salem, MPA

City Planner II

SUBJECT:	TRANSPORTATION REVIEW OF PROFICIENT AUTO PUD

103rd Street (SR 134), from Branan Field-Chaffee Road (SR 23) to Shindler Road, is the directly accessed functionally classified roadway. 103rd Street is a 4-lane divided class I minor arterial in this vicinity and is currently operating at an acceptable LOS B.  103rd Street has a maximum daily service volume of 39,800 vpd and a 2013 daily traffic volume of 12,500 vpd.   This road segment currently has sufficient capacity to accommodate the traffic generated by this development. Access to this site via 103rd Street must be subject to FDOT access management requirements.

The land use of Community/General Commercial (CGC) for this 10.93 acres of ITE Land Use Code 30, Truck Terminal, is estimated to be able to accommodate up to 166,638 square feet of development.  The current proposal for 18,500 square feet of development, which would generate a total of 895 vpd does not exceed the amount of allowable trip generation for this property.

(ITE 30 Truck Terminal – 18,500 square feet)