FLOOR AMENDMENT

Council Member Boyer offers the following floor amendment to File No. 2015-27:

- On page 1, line 17, after “PUD;” insert “PUD REZONING SUBJECT TO CONDITION(S) AND MEMORANDUM;”;

- On page 2, lines 23 and 24, strike “site plan dated November 17, 2014” and insert “second revised site plan dated April 23, 2015”;

- On page 2, line 28, before “Exhibit 2” insert “Second Revised”;

- On page 2, line 28½ insert a new Section 2 to read as follows:

“Section 2.	Rezoning Approved Subject to Conditions and Memorandum. This rezoning is approved subject to the following condition(s).  Such conditions may only be amended through a rezoning.

- All sag lenses, drop lenses and convex lenses shall be prohibited.  Illumination levels at all property lines shall not exceed one-half (.5) foot candles ("f.c.") when the building or parking areas are located adjacent to residential areas, and shall not exceed one (1.0) f.c. when abutting other non-residential properties.  House-side shields and other cutoff reflectors shall be incorporated into the lighting design to meet this design standard.  All lighting lamp sources within parking and pedestrian areas shall be metal halide, compact fluorescent or LED.  The maximum light pole height in all parking areas shall not exceed twenty feet (20’).  An exterior lighting design plan, including a photometrics plan and pole and fixtures schedules, shall be submitted at the time of Verification of Substantial Compliance for review and approval by the Planning and Development Department.

- Outside sales, service or display shall be within ten (10) feet of the building.

- HVAC and cooling condensers shall be mounted on the roof.

- The dumpster shall be screened on three sides with a five (5) foot high masonry wall with a gate that screens the dumpster.

- A six (6) foot high masonry wall, as indicated on the Site Plan dated April 23, 2015, attached hereto as part of Second Revised Exhibit 2, shall be provided by the applicant between the north wall of principal structure and the south property line of the Lot 9.  Said wall shall be located no more than twelve (12) feet from the north wall of the principal structure, and closer if allowed by the Fire Marshall.  There shall be a six (6) foot high transparent fence (such as wrought iron or other metal) at the ends of the masonry wall connecting the wall to the principal structure, with secured access gates(s) that allow only exiting from the area enclosed by the wall and fencing (and no entrance), or an alternative gating system that is acceptable to the Fire Marshall (which is transparent and provides exit only).

- The remainder of the subject property between the masonry wall and the south property line of Lot 9 (approximately 9 feet), shall be maintained by the owner of that property.

- Along the north side of the wall, the applicant shall install eight (8) or nine (9) Leyland Cypress with a minimum height of six (6) feet, at eight (8) to ten (10) feet on center, at an appropriate distance from the wall to allow for maintenance.

- A six (6) foot stockade fence shall be installed by the applicant along the eastern property line of Lot 9 and connecting to the masonry wall installed by the applicant, as shown on Second Revised Exhibit 2.

- The height of the principal structure shall not exceed 23 feet 4 inches (23’-4”) in height along the front of the building facing and parallel to Emerson Street, sloping down to not exceed eighteen feet six inches (18’-6”) in height facing and parallel to the north property line.

Additionally, the PUD shall be subject to the Development Services Division Memorandum dated January 20, 2015 attached hereto as Exhibit 3, or as otherwise approved by the Planning and Development Department.; and

- Attach Second Revised Exhibit 2; and

- Attach Exhibit 3; and

- Renumber the remaining Section(s); and

- On page 1, line 1, amend the introductory sentence to add that the bill was amended as reflected herein.

Form Approved:

/s/ Susan C. Grandin_____

Office of General Counsel

Legislation Prepared By:	Susan C. Grandin

G:\SHARED\LEGIS.CC\2015\Amendments\LUZ Amendments\2015-27 Floor AMEND.doc