LAND USE AND ZONING COMMITTEE AMENDMENT

The Land Use and Zoning Committee offers the following first amendment to File No. 2017-445:

- On page 1, line 17, after “PUD;” insert “PUD REZONING SUBJECT TO CONDITION(S);”;

- On page 2, line 30, strike “Exhibit 3 – Written Description dated April 4, 2017” and insert “Revised Exhibit 3 – Revised Written Description dated July 14, 2017”; and

- On page 3, strike Section 2 in its entirety, and insert a new Section 2 to read as follows:

“Section 2.	Rezoning Approved Subject to Condition(s). This rezoning is approved subject to the following condition(s).  Such conditions control over the written description and may only be amended through a rezoning.

- There shall be a maximum of one ground sign on Normandy Boulevard not to exceed 160 square feet in area and 30 feet in height.

- All sag lenses, drop lenses and convex lenses shall be prohibited. Illuminated levels at all property lines shall not exceed one-half (.5) foot candles (“f.c.”) when the building or parking areas are located adjacent to residential areas, and shall not exceed one (1.0) f.c. when abutting other non-residential properties. All lighting lamp sources within parking and pedestrian areas shall be metal halide, compact fluorescent or LED. The maximum light pole height in all parking areas should not exceed thirty feet (30’ 0”). An exterior lighting design plan, including a photometrics plan, pole and fixtures schedules shall be submitted at the time of Verification of Substantial Compliance for review and approval by the Planning and Development Department.

- The developer shall mount light fixtures on canopies so that the lens cover is recessed or flush with the bottom surface (ceiling) of the canopy.

- New construction shall comply with Chapter 656, Part 12 Landscape and Tree protection Regulations of the Zoning Code.

- Prior to requesting a final building inspection or occupying the facility in any manner, the owner, applicant or developer shall submit to the Planning Department separate certification letters confirming that all horizontal and vertical components of the development have been substantially completed, and all conditions to the development order have been satisfied. This condition shall apply to both phased and non-phased developments.

- Strike Exhibit 3 and attach Revised Exhibit 3.

- On page 1, line 1, amend the introductory sentence to add that the bill was amended as reflected herein.

Form Approved:

/s/ Susan C. Grandin_____

Office of General Counsel

Legislation Prepared By:	Susan C. Grandin

GC-#1150818-v1-2017-445_LUZ_Amd.doc