### M E M O R A N D U M

DATE:		9/29/2017

TO:		Andy Hetzel

City Planner II

FROM:	Soliman Peter Salem

City Planner Supervisor

SUBJECT:	TRANSPORTATION REVIEW OF 2017-0622 THE WELLS CREEK PUD

Philips Highway (SR-5), from the St. Johns County Line to Old St. Augustine Road, is the directly accessed functionally classified roadway. Philips Highway is a 4-lane divided Urban Highway in this vicinity and is currently operating at 41.92% of capacity. This Philips Highway segment has a maximum daily capacity of 65,600 vpd and a 2016 daily traffic volume of 27,500.

This proposal is for up to 2,282 dwelling units of ITE 210 Single Family Homes, which would generate 21,571 vpd, up to 125 dwelling units of ITE 230 Residential Condo/Townhouse, which would generate up to 726 vpd, and up to 152,460 square feet of ITE 820 Shopping Center, which would generate up to 8,933 vpd; a total of 31,230 vpd.

(ITE 210 Single Family Homes- 2,282 DUs)

(ITE 230 Residential Condo/Townhouse- 125 DUs)

(ITE 820 Shopping Center- 125,460 KSF)