LAND USE AND ZONING COMMITTEE AMENDMENT

The Land Use and Zoning Committee offers the following first amendment to File No. 2017-706:

- On page 1, line 15, after “PUD;” insert “PUD REZONING SUBJECT TO CONDITION(S);”;

- On page 1, line 25, strike “Exhibit 1, attached hereto dated August 11, 2017” insert “Revised Exhibit 1, attached hereto dated November 21, 2017”;

- On page 2, line 25 strike “Exhibit 1- Legal Description dated August 11, 2017.” Insert “Revised Exhibit 1- Revised Legal Description dated November 21, 2017.”;

- On page 2, line 28 ½, insert  a new Section 2 to read as follows:

“Section 2.	Rezoning Approved Subject to Condition(s). This rezoning is approved subject to the following condition(s).  Such conditions control over the written description and may only be amended through a rezoning.

- The uncomplementary buffers along the east and south property line shall contain a chain link, wood or vinyl fence which meets the 85% opacity and shall be located on the interior edge of the Natural Buffer, (as defined in Section 656.1222(c)(3), Ordinance Code). A tree survey shall be provided to the Planning and Development Department at the time of substantial verification of the PUD to ensure that a natural buffer meets the minimum requirements.

- All sag lenses, drop lenses and convex lenses shall be prohibited. Illumination levels at all property lines shall not exceed one-half (.5) foot candles (“f.c.”) when the building or parking areas are located adjacent to residential areas, and shall not exceed one (1.0) f.c. when abutting other non-residential properties. All lighting lamp sources within parking and pedestrian areas shall be metal halide, compact fluorescent or LED. An exterior lighting design plan, including a photometrics plan, pole and fixtures schedules shall be submitted at the time of Verification of Substantial Compliance for review and approval by the Planning and Development Department.

- Prior to the final inspection within any phase of development, the owner or their agent shall submit to the Planning and Development Department for its review and approval either (a) an affidavit documenting that all conditions to the development order have been satisfied, or (b) a detailed agreement for the completion of all conditions to the development order.

- Notwithstanding the Development Standards contained in the Written Description, the rear setback shall be expanded to 20’ to be consistent with the rear (Easterly) Natural Buffer.

- Notwithstanding the Development Standards contained in the Written Description, the southern boundary contiguous to the City park property shall have a minimum setback of 15’ and shall be maintained as an undisturbed Natural Buffer and shall contain shade/canopy trees at 25’ on center, which shall be maintained and supplemented as necessary. Said minimum setback may only be reduced to a minimum of 10’ when either the Parks & Recreation Department surpluses the City park property or the Planning and Development Department receives approval from the Director of the Parks & Recreation Department to reduce the setback.”; and

- On page 3, line 1, strike “Exhibit 1” and insert “Revised Exhibit 1”

- Renumber the remaining Section(s).

- Strike Exhibit 1 and attach Revised Exhibit 1.

- On page 1, line 1, amend the introductory sentence to add that the bill was amended as reflected herein.

Form Approved:

/s/ Susan C. Grandin_____

Office of General Counsel

Legislation Prepared By:	Susan C. Grandin

GC-#1170140-v1-2017-706_LUZ_Amd.doc