The Transportation, Energy and Utilities Committee offers the following Substitute to File No. 2017-806:

Introduced by the Council President at the request of the Context Sensitive Streets Standards Committee:

ORDINANCE 2017-806

AN ORDINANCE AMENDING Chapter 654 (Code of subdivision regulations), SECTION 654.116 (DESIGN STANDARDS: ALLEYS) ORDINANCE CODE, TO CLARIFY DESIGN STANDARDS FOR ALLEYS; AMENDING CHAPTER 656 (ZONING CODE), PART 6 (OFF-STREET PARKING AND LOADING REGULATIONS), SECTION 656.607 (DESIGN STANDARDS FOR OFF-STREET PARKING AND LOADING FACILITIES), ORDINANCE CODE, TO INSERT “ON-STREET” PARKING IN THE TITLE, AND TO ADD A NEW SUBSECTION “M” TO PROSCRIBE DIMENSIONS FOR certain ON-STREET PARKING SPACES; AMENDING SECTION 656.608 (OFF-STREET PARKING OF BICYLES), ORDINANCE CODE, TO CORRECT AN ERROR that captures THE VARIETY OF LAYOUTS FOR MULTI-FAMILY HOUSING DEVELOPMENTS; and AMENDING SECTION 656.609 (DESIGN STANDARDS FOR OFF-STREET PARKING FOR BICYCLES), TO ESTABLISH BICYCLE AND MOTORCYCLES PARKING STANDARDS; AMENDING CHAPTER 616 (STREETS AND SIDEWALKS), SECTION 616.102 (BICYCLE RACKS ON SIDEWALKS), ORDINANCE CODE, TO REGULATE THE PLACEMENT OF BICYCLE RACKS; AMENDING CHAPTER 804 (JACKSONVILLE TRAFFIC CODE), Part 9 (Bicycle regulations), SECTION 804.907 (PARKING), ORDINANCE CODE, TO REGULATE BICYCLE PARKING ON SIDEWALKS; PROVIDING AN EFFECTIVE DATE.

BE IT ORDAINED by the Council of the City of Jacksonville:

Section 1.		Amending Chapter 654 (Code of Subdivision Regulations), Section 654.116 (Design standards: alleys), Ordinance Code.  Chapter 654 (Code of Subdivision Regulations), section 654.116 (Design standards; alleys), Ordinance Code, is hereby amended to read as follows:

CHAPTER 654. CODE OF SUBDIVISION REGULATIONS

* * *

Sec. 654.116. – Design standards: alleys.

(a)	Alleys shall be provided in commercial and industrial districts, except that the Department may waive the requirement where other definite and assured provision is made for service access such as off-street loading, unloading and parking consistent with and adequate for the uses proposed. The paved right of way width of an alley shall be as required by the Land Development Procedures Manual.

(b) 	Alleys may be provided in residential districts.

(c) 	Alley intersections and sharp changes in alignment shall be avoided but, where necessary, curves shall be cut off sufficiently to permit safe vehicular, pedestrian and bicycle movement.

(d) 	Dead-end alleys are prohibited.

Section 2.		Chapter 656 (Zoning Code), Ordinance Code, amended. Chapter 656 (Zoning Code), Ordinance Code, is hereby amended to read as follows:

CHAPTER 656. - ZONING CODE.

* * *

PART 6. – OFF-STREET PARKING, ON-STREET PARKING AND LOADING REGULATIONS

SUBPART A. – OFF-STREET PARKING, ON-STREET PARKING AND LOADING FOR MOTOR VEHICLES

* * *

Sec. 656.607. – Design Standards for off-street, on-street parking and loading facilities.

* * *

(d)	Parking Reductions: The following parking reductions are available except for those uses described in Sections 656.604(e) (1) and 656.604(f) (1).

* * *

(4) Motorcycle parking space. Up to 5 percent of required parking may be provided as motorcycle parking space with a minimum length of 7 feet and a minimum width of 4 feet per space dimension of five feet by ten feet per space.

(i)On-street motorcycle parking spaces: On-street marked motorcycle parking spaces shall have a minimum length of 7 feet and a minimum width of 4 feet. Motorcycle parking does not need to be oriented in the same direction as other vehicle parking spaces on the same block.

* * *

(m) The following dimensions are required for on-street parking:

(1)	On-street parallel parking spaces shall have a 7-feet minimum parking stall width including gutter; However, an 8-feet parking stall width is preferred. 7-feet wide stalls are recommended in residential areas or streets with limited right of way.  An 8-feet parking stall width is preferred on functionally classified streets.

(2)	On-street parallel parking shall have a minimum 2-foot step out zone along the adjacent curb, in addition to the minimum sidewalk width requirements provided in the Land Development Procedures Manual.

(3)	On-street perpendicular parking is prohibited.

(4) Back-In or head-in 60-degree angled parking shall contain a minimum 2-foot overhang zone in addition to the minimum sidewalk width requirements provided in the Land Development Procedures Manual.

See Table 1 below for On-Street Parking Dimensions and see Figures C, D and E below for dimension diagrams.

Table 1 - On-Street Parking Dimensions

| Parking Angle | Curb Width | Stall Depth | Stall Width | Stall Length | Car Parking Overhang | Step Out Zone |
| --- | --- | --- | --- | --- | --- | --- |
| 60° (angled – head-in or back-in) | 9.8 | 20.0’ | 8.5’ | 22.0’ | 2.0’ min. | N/A |
| 0° (parallel) | 22.0 | 7.0’ minimum, 8.0’ preferred on functionally classified roadways | 7.0’ minimum, 8.0’ preferred on functionally classified roadways | 22.0’ | N/A | 2.0 |

Figure C – Parallel Parking – step out zone requirements

Source: Jacksonville Design Guidelines and Best Practices Handbook (Section 1: Commercial Development)

Figure D – Angled Parking – Car parking overhang requirements Source: Jacksonville Design Guidelines and Best Practices Handbook (Section 1: Commercial Development)

Figure E – On-street parking diagrams

* * *

SUBPART B. – OFF-STREET PARKING FOR BICYCLES

Section 656.608. 	Off-Street parking of bicycles.

The required number of off-street parking spaces for bicycles is as follows:

(a) Residential uses:

| (1)Multiple-family dwellings (with structured parking) Individual garages shall be credited 2 bedrooms per individual garage. Each bay located in a garage shall be credited 2 rooms per bay. | 0.025 spaces on-site per bedroom(2 spaces minimum) and 0.1 spaces in structured parking per bedroom |
| --- | --- |
| (2) Multiple-family dwellings (no structured parking) Individual garages shall be credited 2 bedrooms per individual garage. | 0.125 spaces on-site per bedroom (2 spaces minimum) |
| (23)Rooming and boarding houses | 1 per 3 rooms |
| (34)Mobile home park | 2% of the required off-street motor vehicle parking |
| (45)Convents and monasteries | 1 per 5 rooms |
| (56)Fraternity and sorority houses | 0.5 spaces per bedroom (2 spaces minimum) |
| (67)Hotels and motels | 1 per 20 employees |

* * *

Sec. 656.609 – Design standards for off-street parking for bicycles.

Off-street parking facilities for bicycles shall: follow the City of Jacksonville Bicycle Parking Standards located in Section 3.0 of the Land Development Procedures Manual. The Bicycle Parking Standards provide the location, design, placement and installation requirements.

Bicycle parking facilities shall:

(a) Be designed to allow each bicycle to be supported by its frame in two places.

(b) Be designed to allow the frame and wheels of each bicycle to be secured by a lock against theft.

(c) Be designed to avoid damage to the bicycles.

(d) Be anchored to resist rust or corrosion, or removal by vandalism.

(e) Accommodate a range of bicycle shapes and sizes and to facilitate easy locking without interfering with adjacent bicycles.

(f) Be located to prevent damage to bicycles by cars.

(g) Be consistent with the surroundings in color and design and be incorporated whenever possible into buildings or street furniture design.

(h) Be located in convenient, highly-visible, active, well-lighted areas.

(i) Be located so as not to interfere with pedestrian flow on the sidewalk and should not be placed directly in front of entrances, doors or disabled parking spaces movements.

(j) Be located as near to the principal entrance of the building as practicable. Bicycle parking should be located as close to the entrance of the building it serves as the nearest car parking space.

(k) Provide safe access from the spaces to the right-of-way or bicycle lane.

(l) Have at least 5 feet of clearance between any bicycle rack and a driveway or curb cut.

* * *

  - Share Link

  - Print

  - Download (docx)

  - Email

  - Compare

Section 3.		Amending Section 616.102 (Bicycle racks on sidewalks), Chapter 616 (Streets and Sidewalks), Ordinance Code. Section 616.102 (Bicycle racks on sidewalks), Chapter 616 (Streets and Sidewalks), Ordinance Code, is hereby amended to read as follows:

CHAPTER 616.	STREETS AND SIDEWALKS.

* * *

Sec. 616.102. – Bicycle racks on sidewalks.

No person shall place any A bicycle rack shall not be placed on any sidewalk or in the space between the sidewalk and the roadway of any street without obtaining a permit from the City Council for that purpose. The City Council may grant a permit under such terms and conditions as determined to it shall seem advisable for the protection of the interests of the City. Violation of this Section shall constitute a cClass C offense.

Section 4.		Amending Section 804.907 (Parking), Chapter 804 (Jacksonville Traffic Code), Ordinance Code. Section 804.907 (Parking), Chapter 804 (Jacksonville Traffic Code), Ordinance Code, is hereby amended to read as follows:

CHAPTER 804.	JACKSONVILLE TRAFFIC CODE.

* * *

PART 9. BICYCLE REGULATIONS

* * *

Sec. 804.907. – Parking.

A person may stop, stand or park a bicycle on a sidewalk, if the bicycle does not impede the normal and reasonable movement of pedestrians or other traffic on the sidewalk. No person shall stand or park a bicycle on a sidewalk within a business district.  Violation of this Section shall constitute a class A offense.

Section 5.		Effective Date.  This ordinance shall become effective upon signature by the Mayor or upon becoming effective without the Mayor’s signature.

Form Approved:

/s/Cherry Shaw Pollock_____________

Office of General Counsel

Legislation prepared by:  Cherry Shaw Pollock

GC-#1211831-v2-2017-806_Substitute_052118.doc