### M E M O R A N D U M

DATE:		3/27/2018

TO:		Andy Hetzel

City Planner Supervisor

FROM:	Soliman Peter Salem

City Planner Supervisor

SUBJECT:	TRANSPORTATION REVIEW OF 2018-153 LIBERTY SQUARE PUD

Chaffee Road, from Crystal Springs Road to Normandy Boulevard, is the directly accessed functionally classified roadway. Chaffee Road is a 2-lane undivided Class I Minor Arterial in this vicinity and is currently operating at 80.50% of capacity. This proposal is for 200 dwelling units of ITE 210 Single Family Homes, which would generate 1,888 vpd. This Chaffee Road segment has a maximum daily capacity of 15,930 vpd and a 2017 daily traffic volume of 12,823 vpd.

(ITE 210 Single Family Homes– 200 DUs)

*The Transportation Planning Division Conditions the following for approval:

1) Left and right turn lanes shall be provided on New World Avenue at the proposed entrance roadways for Parcel C and D. The turn lanes will be designed to FDOT standards based on the design speed (posted plus 5 mph minimum), and require an overlay of the entire construction limits and include extruded thermoplastic pavement markings, and reflective pavement markers. Left turn Queue lengths shall be a minimum of 100’