LAND USE AND ZONING COMMITTEE AMENDMENT

The Land Use and Zoning Committee offers the following first amendment to File No. 2018-373:

- On page 1, line 14, after “CODE;” insert “SIGN WAIVER SUBJECT TO CONDITIONS;”; and

- On page 2, line 30, strike “The” and insert “As conditioned herein, the”; and

- On page 3, line 25½, insert a new Section 2 to read as follows:

“Section 2. Sign Waiver Approved Subject to Conditions.  This sign waiver is approved subject to the following conditions, which are based on International Sign Association recommendations for brightness levels for signs that utilize computer-generated messages (or some other electronic means of changing copy including displays using incandescent lamps, LEDs, LCDs or a flipper matrix), as published in compilation research reports dated December 2010 and August 2016:

- The illuminance of the sign shall be measured with an illuminance meter set to measure footcandles, accurate to at least two decimals.  Illuminance shall be measured with the sign off, and again with the sign displaying a white image for a full color capable sign, or a solid message for a single color sign.  All measurements shall be taken perpendicular to the face of the sign at a distance of ninety-two (92) feet. This distance is based on a sign face measuring 85.38 square feet, as depicted on Exhibit 4, attached hereto.  If the size of the sign face is modified, the measurement distance shall be calculated as the square root of the area of the sign multiplied by one hundred (100).

- The difference between the off and solid message measurements using the above criteria shall not exceed 0.3 footcandles.

- The sign shall be equipped with a sensor or other device that automatically determines the ambient illumination, and the sign shall be programmed to automatically dim according to ambient light conditions, or if such automatic programming is unavailable, the sign must include the technological capability to adjust the illumination to comply with the 0.3 footcandle measurement at all times.

- Prior to the final inspection for the sign permit, the owner or their agent shall submit to the Planning and Development Department for its review, an affidavit documenting that all conditions as stated herein have been satisfied.”; and

- Renumber the remaining Sections.

- On page 1, line 1, amend the introductory sentence to add that the bill was amended as reflected herein.

Form Approved:

/S/ Shannon K. Eller

Office of General Counsel

Legislation Prepared By:	Shannon K. Eller

GC-#1227680-v1-2018-373_LUZ_Amd.doc