Introduced by Council Members Boyer and Love and Co-Sponsored by  Council Member Ferraro:

ORDINANCE 2019-331

AN ORDINANCE AMENDING chapter 652 (FLOODPLAIN MANAGEMENT ORDINANCE), ordinance code; amending PART 2 (APPLICABILITY), section 652.202 (areas to which this chapter applies), PART 5 (SITE PLANS AND CONSTRUCTION DOCUMENTS), sections 652.501 (information for development in flood hazard areas), 652.503 (ADDITIONAL ANALYSES and CERTIFICATION), and 652.504 (submission of additional data and contingent approvals), PART 7 (VARIANCE AND APPEALS), section 652.704 (restrictions in floodways), PART 9 (DEFINITIONS), section 652.904 (definitions), and part 10 (flood resistant development), sections 652.1204 (limitations on sites in regulatory floodways), 652.1601 (general requirements for other development), 652.1602 (fences in regulated floodways), 652.1603 (retaining walls, sidewalks and driveways in regulated floodways), and 652.1604 (roads and watercourse crossings in regulated floodways) to PROVIDE 25-foot floodway setback REGULATIONS; amending part 5 (SITE PLANS AND CONSTRUCTION DOCUMENTS), SECTION 652.502 (INFORMATION IN FLOOD HAZARD AREAS WITHOUT BASE FLOOD ELEVATIONS (APPROXIMATE ZONE a)) TO ADDRESS CERTAIN FINISHED FLOOR ELEVATIONS, AND section 652.503 (additional analyses and certifications) to prohibit increase in the base flood elevation in riverine flood hazard areas; AMENDING PART 7 (VARIANCES AND APPEALS), SECTIONS 652.701 (GENERAL), 652.702 (APPEALS), 652.703 (LIMITATIONS ON AUTHORITY TO GRANT VARIANCES), 652.707 (CONSIDERATIONS FOR ISSUANCE OF VARIANCES), AND 652.708 (CONDITIONS FOR ISSUANCE OF VARIANCES) TO AUTHORIZE THE PLANNING AND DEVELOPMENT DEPARTMENT DIRECTOR AND THE COUNCIL TO HEAR certain APPEALS AND VARIANCES; AMENDING PART 5 (SITE PLANS AND CONSTRUCTION DOCUMENTS), SECTION 652.501, AND part 10 (flood resistant development), section 652.1205 (limitations on placement of fill) to PROVIDE FILL REQUIREMENTS; AMENDING PART 10 (flood resistant development) TO CREATE SECTION 652.1207 TO ADDRESS CERTAIN FINISHED FLOOR ELEVATIONS; PROVIDING FOR SEVERABILITY; PROVIDING AN EFFECTIVE DATE.

WHEREAS, the Storm Resiliency & Infrastructure Development Review Committee has recommended certain changes to the City of Jacksonville’s floodplain management regulations regarding requirements for fill, requirements for a floodway setback, and requirements for the finished floor elevation in special flood hazard areas, to protect the health, safety, and welfare of the citizens of the City of Jacksonville; now, therefore

BE IT ORDAINED by the Council of the City of Jacksonville:

Section 1. CHAPTER 652 (FLOODPLAIN MANAGEMENT ORDINANCE), Ordinance Code, Amended.  CHAPTER 652 (FLOODPLAIN MANAGEMENT ORDINANCE), Ordinance Code, is hereby amended to read as follows:

CHAPTER 652 – FLOODPLAIN MANAGEMENT ORDINANCE

* * *

PART 2. – APPLICABILITY

* * *

Sec. 652.202 - Areas to which this Chapter applies. This Chapter shall apply to all flood hazard areas and Adjusted Special Flood Hazard Areas within the City of Jacksonville as established in Section 652.203 of this Chapter, and to all floodways and floodway setbacks, as provided in this Chapter.

* * *

PART 5. – SITE PLANS AND CONSTRUCTION DOCUMENTS

Sec. 652.501. - Information for development in flood hazard areas.  The site plan or construction documents for any development subject to the requirements of this Chapter shall be drawn to scale and shall include, as applicable to the proposed development:

(a) Delineation of flood hazard areas, Adjusted SFHAs, floodway boundaries, floodway setbacks and flood zone(s), base flood elevation(s), and ground elevations if necessary for review of the proposed development; if the proposed development will cause a reconfiguration of the flood hazard area due to grading, filling, channel alteration or relocation, development of a stormwater management system, or the excavation of a lake, the Floodplain Administrator shall require the applicant to submit and obtain approval from FEMA of a Conditional Letter of Map Revision.

* * *

(i)	Where the placement of fill is proposed, the amount, type, and source of fill material; compaction specifications; a description of the intended purpose of the fill areas; permeability analysis; and evidence that the proposed fill areas are the minimum necessary to achieve the intended purpose.

* * *

Sec. 652.502. - Information in flood hazard areas without base flood elevations (approximate Zone A).  Where flood hazard areas are delineated on the FIRM and base flood elevation data have not been provided, the Floodplain Administrator shall:

* * *

(c)	Where base flood elevation and floodway data are not available from another source, where the available data are deemed by the Floodplain Administrator to not reasonably reflect flooding conditions, or where the available data are known to be scientifically or technically incorrect or otherwise inadequate:

* * *

(2) Specify that the base flood elevation is the higher of three feet above the highest adjacent grade plus one two foot at the location of the development, as required by Section 652.1207, 18 inches above the higher crown of an adjacent road, or three feet above the highest known flood level.

* * *

Sec. 652.503. - Additional analyses and certifications. As applicable to the location and nature of the proposed development activity, and in addition to the requirements of this Section, the applicant shall have the following analyses signed and sealed by a Florida licensed engineer for submission with the site plan and construction documents:

(a) For development activities proposed to be located in a regulatory floodway, or a floodway setback, a floodway encroachment analysis that demonstrates that the encroachment of the proposed development will not cause any increase in base flood elevations; where the applicant proposes to undertake development activities that do increase base flood elevations, the applicant shall submit such analysis to FEMA as specified in Section 652.504 of this Chapter and shall submit the Conditional Letter of Map Revision, if issued by FEMA, with the site plan and construction documents.

(b) For development activities proposed to be located in a riverine flood hazard area for which base flood elevations are included in the Flood Insurance Study or on the FIRM and floodways have not been designated, hydrologic and hydraulic analyses that demonstrate that the cumulative effect of the proposed development, when combined with all other existing and anticipated flood hazard area encroachments, will not increase the base flood elevation more than one foot at any point within the community. This requirement does not apply in isolated flood hazard areas not connected to a riverine flood hazard area or in flood hazard areas identified as Zone AO or Zone AH.

* * *

Sec. 652.504. - Submission of additional data and contingent approvals.

* * *

(b) Final acceptance of subdivision improvements shall not occur, final construction plans for development in floodways, or in floodway setbacks, shall not be approved, and Certificates of Occupancy shall not be issued until such time as FEMA has issued a Letter of Map Change, except in the case of Conditional Letters of Map Revision issued by FEMA, in which case final acceptance of subdivision improvements and Certificates of Occupancy shall not be issued until such time as the permittee submits to FEMA the as-built documentation and obtained a Letter of Map Revision.

(c) Except for development in a floodway, or in a floodway setback, the Floodplain Administrator may grant an extension or extension for the time frame for obtaining a Letter of Map Change where the applicant demonstrates that such letters have been diligently pursued but not obtained due to circumstances beyond the control of the applicant.

* * *

PART 7. – VARIANCES AND APPEALS

Sec. 652.701. - General.

The Subdivision Standards Policy and Advisory Committee ("SSPAC") Director of the Planning and Development Department shall hear and decide on requests for appeals and requests for variances from the strict application of this Chapter. Pursuant to F.S. § 553.73(5), the SSPAC Director of the Planning and Development Department shall hear and decide on requests for appeals and requests for variances from the strict application of the flood resistant construction requirements of the Florida Building Code. This Section does not apply to Section 3109 of the Florida Building Code, Building.

Sec. 652.702. – Appeals.  The SSPAC Director of the Planning and Development Department shall hear and decide appeals when it is alleged there is an error in any requirement, decision, or determination made by the Floodplain Administrator in the administration and enforcement of this Chapter. Any person aggrieved by the decision of SSPAC the Director of the Planning and Development Department may appeal such decision to the Circuit Court, as provided by Florida Statutes Council using the procedures, timeframes, and standard of review in Section 656.135, Ordinance Code.

Sec. 652.703. - Limitations on authority to grant variances.  The SSPAC Director of the Planning and Development Department shall base its decisions on variances on technical justifications submitted by applicants, the considerations for issuance in Section 652.707, Ordinance Code, the conditions of for issuance set forth in Section 652.708, Ordinance Code, and the comments and recommendations of the Floodplain Administrator and the Building Official. The SSPAC Director of the Planning and Development Department has the right to attach such conditions as it the Director deems necessary to further the purposes and objectives of this Chapter.

Sec. 652.704. - Restrictions in floodways and floodway setbacks.	A variance shall not be issued for any proposed development in a floodway, or in a floodway setback, if any increase in base flood elevations would result, as evidenced by the applicable analyses and certifications required in Section 652.503, Ordinance Code.

* * *

Sec. 652.707. - Considerations for issuance of variances.  In reviewing requests for variances, the SSPAC Director of the Planning and Development Department shall consider all technical evaluations, all relevant factors, all other applicable provisions of the Florida Building Code, this Chapter, and the following:

* * *

Sec. 652.708. - Conditions for issuance of variances.  Variances shall be issued only upon:

* * *

(b) Determination by the SSPAC Director of the Planning and Development Department that:

* * *

PART 9. – DEFINITIONS

SECTION 652.900. - GENERAL

* * *

Sec. 652.904. - Definitions.

* * *

Floodway encroachment analysis. An engineering analysis of the impact that a proposed encroachment into a floodway, or into a floodway setback, is expected to have on the floodway boundaries and base flood elevations; the evaluation shall be prepared by a qualified Florida licensed engineer using standard engineering methods and models.

Floodway setback. The area between the outer boundary of the regulatory floodway associated with natural named wetland systems shown on the FIRM and a line parallel thereto at a distance of 25 feet. The purpose of this 25-foot floodway setback is to minimize encroachments, and to protect floodplain storage and natural floodplain functions.

* * *

PART 10. – FLOOD RESISTANT DEVELOPMENT

* * *

SECTION 652.1100. – SUBDIVISIONS

* * *

Sec. 652.1102. - Subdivision plats.	Where any portion of proposed subdivisions, including manufactured home parks and subdivisions, lies within a flood hazard area, the following shall be required:

(a) Delineation of flood hazard areas, Adjusted SFHAs, floodway boundaries, floodway setbacks and flood zones, and design flood elevations, as appropriate, shall be shown on preliminary plats;

* * *

SECTION 652.1200. – SITE IMPROVEMENTS, UTILITIES AND LIMITATIONS

* * *

Sec. 652.1204. - Limitations on sites in regulatory floodways, and floodway setbacks.

No development, including but not limited to site improvements, and land disturbing activity involving fill or regrading, shall be authorized in the regulatory floodway, or in the floodway setback, unless the floodway encroachment analysis required in Section 652.503(a), Ordinance Code, demonstrates that the proposed development or land disturbing activity will not result in any increase in the base flood elevation.

Sec. 652.1205. - Limitations on placement of fill.  All fill shall be AASHTO Class A-3 Soil unless a Certified Geotechnical Engineer provides a pre-development vs. post-development analysis showing that alternative fill will not adversely impact groundwater levels on adjacent property.  Subject to the limitations of this Chapter, fill shall be designed to be stable under conditions of flooding including rapid rise and rapid drawdown of floodwaters, prolonged inundation, and protection against flood-related erosion and scour. In addition to these requirements, if intended to support buildings and structures (Zone A only), fill shall comply with the requirements of the Florida Building Code.

* * *

Sec. 652.1207. – Finished floor elevation in special flood hazard areas.  The finished floor elevation in special flood hazard areas shall be two feet above the base flood elevation.  If there is a conflict between this Section and any other provisions of the City of Jacksonville Ordinance Code, this Section shall supersede such other provisions.

* * *

SECTION 652.1600. – OTHER DEVELOPMENT

Sec. 652.1601. - General requirements for other development. All development, including man-made changes to improved or unimproved real estate for which specific provisions are not specified in this Chapter or the Florida Building Code, shall:

* * *

(b) Meet the limitations of Section 652.1204, Ordinance Code if located in a regulated floodway, or in a floodway setback;

* * *

Sec. 652.1602. - Fences in regulated floodways, or in floodway setbacks. Fences in regulated floodways, or in floodway setbacks, that have the potential to block the passage of floodwaters, such as stockade fences and wire mesh fences, shall meet the limitations of Section 652.1204, Ordinance Code.

Sec. 652.1603. - Retaining walls, sidewalks and driveways in regulated floodways, or in floodway setbacks. Retaining walls and sidewalks and driveways that involve the placement of fill in regulated floodways, or in floodway setbacks, shall meet the limitations of Section 652.1204, Ordinance Code.

Sec. 652.1604. - Roads and watercourse crossings in regulated floodways, or in floodway setbacks. Roads and watercourse crossings, including roads, bridges, culverts, low-water crossings and similar means for vehicles or pedestrians to travel from one side of a watercourse to the other side, that encroach into regulated floodways, or into floodway setbacks, shall meet the limitations of Section 652.1204, Ordinance Code. Alteration of a watercourse that is part of a road or watercourse crossing shall meet the requirements of Section 652.503(c), Ordinance Code.

* * *

Section 2.	 	Severability. The provisions of this Ordinance are intended to be severable and if any provision is declared invalid or unenforceable by a court of competent jurisdiction, such provision shall be severed and the remainder shall continue in full force and effect with the Ordinance being deemed amended to the least degree legally permissible.

Section 3.		Effective Date. This Ordinance shall become effective upon signature by the Mayor or upon becoming effective without the Mayor’s signature.

Form Approved:

/s/ Shannon K. Eller_____

Office of General Counsel

Legislation Prepared By:	Shannon K. Eller

GC-#1276259-v1-CHAPTER_652_FLOODPLAIN_MANAGEMENT_UPDATE